## Slide 1: The Network Core
mesh of interconnected routers
the fundamental question: how is data transferred through net?
  circuit switching: dedicated circuit per call: telephone net
  packet-switching: data sent thru net in discrete “chunks”

## Slide 2: Network Core: Circuit Switching
End-end resources reserved for “call”
link bandwidth, switch capacity
dedicated resources: no sharing
circuit-like (guaranteed) performance
call setup required

## Slide 3: Network Core: Circuit Switching
network resources (e.g., bandwidth) divided into “pieces”
pieces allocated to calls
resource piece idle if not used by owning call (no sharing)
dividing link bandwidth into “pieces”
  frequency division
  time division

## Slide 4: Circuit Switching: FDM and TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 5: Network Core: Packet Switching
each end-end data stream divided into packets
user A, B packets share network resources
each packet uses full link bandwidth
resources used as needed
resource contention:
aggregate resource demand can exceed amount available
congestion: packets queue, wait for link use
store and forward: packets move one hop at a time
  Node receives complete packet before forwarding
Bandwidth division into “pieces”
Dedicated allocation
Resource reservation

## Slide 6: Packet Switching: Statistical Multiplexing
Sequence of A & B packets does not have fixed pattern, shared on demand  statistical multiplexing.
TDM: each host gets same slot in revolving TDM frame.
A
B
C
10 Mb/s
Ethernet
1.5 Mb/s
D
E
statistical multiplexing
queue of packets
waiting for output
link

## Slide 7: Packet-switching: store-and-forward
Takes L/R seconds to transmit (push out) packet of L bits on to link or R bps
Entire packet must arrive at router before it can be transmitted on next link: store and forward
delay = 3L/R (assuming zero propagation delay)
Example:
L = 7.5 Mbits
R = 1.5 Mbps
delay = 15 sec
R
R
R
L
more on delay shortly …

## Slide 8: Packet switching versus circuit switching
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active less than .0004
Packet switching allows more users to use network!
N users
1 Mbps link
Q: how did we get value 0.0004?

## Slide 9: Packet switching versus circuit switching
Great for bursty data
  resource sharing
  simpler, no call setup
Excessive congestion: packet delay and loss
  protocols needed for reliable data transfer, congestion control
Q: How to provide circuit-like behavior?
  bandwidth guarantees needed for audio/video apps
  still an unsolved problem (chapter 7)
Is packet switching a “slam dunk winner?”
Q: human analogies of reserved resources (circuit switching) versus on-demand allocation (packet-switching)?

## Slide 10: How do loss and delay occur?
packets queue in router buffers
packet arrival rate to link exceeds output link capacity
packets queue, wait for turn
A
B
packet being transmitted (delay)
packets queueing (delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 11: Four sources of packet delay
1. nodal processing:
  check bit errors
  determine output link
A
B
propagation
transmission
nodal
processing
queueing
2. queueing
  time waiting at output link for transmission
  depends on congestion level of router

## Slide 12: Delay in packet-switched networks
3. Transmission delay:
R=link bandwidth (bps)
L=packet length (bits)
time to send bits into link = L/R
4. Propagation delay:
d = length of physical link
s = propagation speed in medium (~2x108 m/sec)
propagation delay = d/s
A
B
propagation
transmission
nodal
processing
queueing
Note: s and R are very different quantities!

## Slide 13: Nodal delay
dproc = processing delay
  typically a few microsecs or less
dqueue = queuing delay
  depends on congestion
dtrans = transmission delay
  = L/R, significant for low-speed links
dprop = propagation delay
  a few microsecs to hundreds of msecs

## Slide 14: “Real” Internet delays and routes
What do “real” Internet delay & loss look like?
Traceroute program: provides delay measurement from source to router along end-end Internet path towards destination. For all i:
  sends three packets that will reach router i on path towards destination
  router i will return packets to sender
  sender times interval between transmission and reply.
3 probes
3 probes
3 probes

## Slide 15: “Real” Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
Three delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic
link

## Slide 16: Queueing delay (revisited)
R=link bandwidth (bps)
L=packet length (bits)
a=average packet arrival rate
traffic intensity = La/R
La/R ~ 0: average queueing delay small
La/R -> 1: delays become large
La/R > 1: more “work” arriving than can be serviced, average delay infinite!

## Slide 17: Packet loss
queue (aka buffer) preceding link in buffer has finite capacity
when packet arrives to full queue, packet is dropped (aka lost)
lost packet may be retransmitted by previous node, by source end system, or not retransmitted at all

## Slide 18: Throughput
throughput: rate (bits/time unit) at which bits transferred between sender/receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)
server sends bits
(fluid) into pipe

## Slide 19: Throughput (more)
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
link on end-end path that constrains end-end throughput
bottleneck link

## Slide 20: Throughput: Internet scenario
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck

## Slide 21: Sockets
process sends/receives messages to/from its socket
socket analogous to door
  sending process shoves message out door
  sending process relies on transport infrastructure on other side of door which brings message to socket at receiving process
process
TCP with
buffers,
variables
socket
host or
server
process
TCP with
buffers,
variables
socket
host or
server
Internet
controlled
by OS
controlled by
app developer

## Slide 22: Addressing processes
to receive messages, process must have identifier
host device has unique32-bit IP address
Q: does IP address of host on which process runs suffice for identifying the process?
  Answer: NO, many processes can be running on same host
identifier includes both IP address and port numbers associated with process on host.
Example port numbers:
  HTTP server: 80
  Mail server: 25
to send HTTP message to gaia.cs.umass.edu web server:
  IP address: 128.119.245.12
  Port number: 80

## Slide 23: App-layer protocol defines
Types of messages exchanged,
  e.g., request, response
Message syntax:
  what fields in messages & how fields are delineated
Message semantics
  meaning of information in fields
Rules for when and how processes send & respond to messages

## Slide 24: What should be considered for apps?
Data loss
some apps (e.g., audio) can tolerate some loss
other apps (e.g., file transfer, telnet) require 100% reliable data transfer
Timing
some apps (e.g., Internet telephony, interactive games) require low delay to be “effective”
Bandwidth
some apps (e.g., multimedia) require minimum amount of bandwidth to be “effective”
other apps (“elastic apps”) make use of whatever bandwidth they get

## Slide 25: Transport service requirements of common apps
Application
file transfer
e-mail
Web documents
real-time audio/video
stored audio/video
interactive games
instant messaging
Data loss
no loss
no loss
no loss
loss-tolerant
loss-tolerant
loss-tolerant
no loss
Bandwidth
elastic
elastic
elastic
audio: 5kbps-1Mbps
video:10kbps-5Mbps
same as above
few kbps up
elastic
Time Sensitive
no
no
no
yes, 100’s msec
yes, few secs
yes, 100’s msec
yes and no

## Slide 26: Internet transport protocols services
TCP service:
connection-oriented: setup required between client and server processes
reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
does not provide: timing, minimum bandwidth guarantees
UDP service:
unreliable data transfer between sending and receiving process
does not provide: connection setup, reliability, flow control, congestion control, timing, or bandwidth guarantee
Q: why bother? Why is there a UDP?

## Slide 27: Internet apps: application, transport protocols
Application
e-mail
remote terminal access
Web
file transfer
streaming multimedia
Internet telephony
Application
layer protocol
SMTP [RFC 2821]
Telnet [RFC 854]
HTTP [RFC 2616]
FTP [RFC 959]
proprietary
(e.g. RealNetworks)
proprietary
(e.g., Vonage,Dialpad)
Underlying
transport protocol
TCP
TCP
TCP
TCP
TCP or UDP
typically UDP

## Slide 28: P2P file sharing
Example
Alice runs P2P client application on her notebook computer
Intermittently connects to Internet; gets new IP address for each connection
Asks for “Hey Jude”
Application displays other peers that have copy of Hey Jude.
Alice chooses one of the peers, Bob.
File is copied from Bob’s PC to Alice’s notebook: HTTP
While Alice downloads, other users uploading from Alice.
Alice’s peer is both a Web client and a transient Web server.
All peers are servers = highly scalable!

## Slide 29: P2P: centralized directory
original “Napster” design
1) when peer connects, it informs central server:
  IP address
  content
2) Alice queries for “Hey Jude”
3) Alice requests file from Bob
centralized
directory server
peers
Alice
Bob
1
1
1
1
2
3

## Slide 30: P2P: problems with centralized directory
Single point of failure
Performance bottleneck
Copyright infringement
file transfer is decentralized, but locating content is highly centralized

## Slide 31: Query flooding: Gnutella
fully distributed
  no central server
public domain protocol
many Gnutella clients implementing protocol
overlay network: graph
edge between peer X and Y if there’s a TCP connection
all active peers and edges is overlay net
Edge is not a physical link
Given peer will typically be connected with < 10 overlay neighbors

## Slide 32: Gnutella: protocol
Query
QueryHit
Query
Query
QueryHit
Query
Query
QueryHit
File transfer:
HTTP
Query message sent over existing TCP connections
peers forward Query message
QueryHit sent over reverse path
Scalability:
limited scope flooding

## Slide 33: Gnutella: Peer joining
Joining peer X must find some other peer in Gnutella network: use list of candidate peers
X sequentially attempts to make TCP with peers on list until connection setup with Y
X sends Ping message to Y; Y forwards Ping message.
All peers receiving Ping message respond with Pong message
X receives many Pong messages. It can then setup additional TCP connections
Peer leaving: see homework problem!

## Slide 34: Hierarchical Overlay
between centralized index, query flooding approaches
each peer is either a group leader or assigned to a group leader.
  TCP connection between peer and its group leader.
  TCP connections between some pairs of group leaders.
group leader tracks content in its children

## Slide 35: KaZaA: Querying
Each file has a hash and a descriptor
Client sends keyword query to its group leader
Group leader responds with matches:
  For each match: metadata, hash, IP address
If group leader forwards query to other group leaders, they respond with matches
Client then selects files for downloading
  HTTP requests using hash as identifier sent to peers holding desired file

## Slide 36: KaZaA tricks
Limitations on simultaneous uploads
Request queuing
Incentive priorities
Parallel downloading
For more info:
J. Liang, R. Kumar, K. Ross, “Understanding KaZaA,”
(available via cis.poly.edu/~ross)

## Slide 37: File Distribution: Server-Client vs P2P
Question : How much time to distribute file from one server to N peers?
us
u2
d1
d2
u1
uN
dN
Server
Network (with
abundant bandwidth)
File, size F
us: server upload bandwidth
ui: peer i upload bandwidth
di: peer i download bandwidth

## Slide 38: File distribution time: server-client
us
u2
d1
d2
u1
uN
dN
Server
Network (with
abundant bandwidth)
F
server sequentially sends N copies:
  NF/us time
client i takes F/di time to download
increases linearly in N
(for large N)
= dcs = max { NF/us, F/min(di) }
i
Time to distribute F
to N clients using
client/server approach

## Slide 39: File distribution time: P2P
us
u2
d1
d2
u1
uN
dN
Server
Network (with
abundant bandwidth)
F
server must send one copy: F/us time
client i takes F/di time to download
NF bits must be downloaded (aggregate)
fastest possible upload rate: us + Sui
dP2P = max { F/us, F/min(di) , NF/(us + Sui) }
i

## Slide 40
Comparing Client-server, P2P architectures

## Slide 41: Socket programming
Socket API
introduced in BSD4.1 UNIX, 1981
explicitly created, used, released by apps
client/server paradigm
two types of transport service via socket API:
  unreliable datagram
  reliable, byte stream-oriented
a host-local,
application-created,
OS-controlled interface (a “door”) into which
application process can both send and
receive messages to/from another application process
socket
Goal: learn how to build client/server application that communicate using sockets

## Slide 42: Socket-programming using TCP
Socket: a door between application process and end-end-transport protocol (UCP or TCP)
TCP service: reliable transfer of bytes from one process to another
process
TCP with
buffers,
variables
socket
controlled by
application
developer
controlled by
operating
system
host or
server
process
TCP with
buffers,
variables
socket
controlled by
application
developer
controlled by
operating
system
host or
server
internet

## Slide 43: Socket programming with TCP
Client must contact server
server process must first be running
server must have created socket (door) that welcomes client’s contact
Client contacts server by:
creating client-local TCP socket
specifying IP address, port number of server process
When client creates socket: client TCP establishes connection to server TCP
When contacted by client, server TCP creates new socket for server process to communicate with client
  allows server to talk with multiple clients
  source port numbers used to distinguish clients (more in Chap 3)
TCP provides reliable, in-order
transfer of bytes (“pipe”)
between client and server
application viewpoint

## Slide 44: Client/server socket interaction: TCP
wait for incoming
connection request
connectionSocket =
welcomeSocket.accept()
create socket,
port=x, for
incoming request:
welcomeSocket =
ServerSocket()
create socket,
connect to hostid, port=x
clientSocket =
Socket()
close
connectionSocket
read reply from
clientSocket
close
clientSocket
Server (running on hostid)
Client
send request using
clientSocket
read request from
connectionSocket
write reply to
connectionSocket
TCP
connection setup

## Slide 45: Socket programming with UDP
UDP: no “connection” between client and server
no handshaking
sender explicitly attaches IP address and port of destination to each packet
server must extract IP address, port of sender from received packet
UDP: transmitted data may be received out of order, or lost
application viewpoint
UDP provides unreliable transfer
of groups of bytes (“datagrams”)
between client and server

## Slide 46: Client/server socket interaction: UDP
close
clientSocket
Server (running on hostid)
read reply from
clientSocket
create socket,
clientSocket =
DatagramSocket()
Client
Create, address (hostid, port=x,
send datagram request
using clientSocket
create socket,
port=x, for
incoming request:
serverSocket =
DatagramSocket()
read request from
serverSocket
write reply to
serverSocket
specifying client
host address,
port number

## Slide 47: Multiplexing/demultiplexing
application
transport
network
link
physical
P1
application
transport
network
link
physical
application
transport
network
link
physical
P2
P3
P4
P1
host 1
host 2
host 3
= process
= socket
delivering received segments
to correct socket
Demultiplexing at rcv host:
gathering data from multiple
sockets, enveloping data with
header (later used for
demultiplexing)
Multiplexing at send host:

## Slide 48: How demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries 1 transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(message)
other header fields
TCP/UDP segment format

## Slide 49: Connectionless demultiplexing
Create sockets with port numbers:
DatagramSocket mySocket1 = new DatagramSocket(12534);
DatagramSocket mySocket2 = new DatagramSocket(12535);
UDP socket identified by two-tuple:
(dest IP address, dest port number)
When host receives UDP segment:
  checks destination port number in segment
  directs UDP segment to socket with that port number
IP datagrams with different source IP addresses and/or source port numbers directed to same socket

## Slide 50: Connectionless demux (cont)
DatagramSocket serverSocket = new DatagramSocket(6428);
Client
IP:B
P2
client
IP: A
P1
P1
P3
server
IP: C
SP: 6428
DP: 9157
SP: 9157
DP: 6428
SP: 6428
DP: 5775
SP: 5775
DP: 6428
SP provides “return address”

## Slide 51: Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
recv host uses all four values to direct segment to appropriate socket
Server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
Web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request

## Slide 52: Connection-oriented demux (cont)
Client
IP:B
P1
client
IP: A
P1
P2
P4
server
IP: C
SP: 9157
DP: 80
SP: 9157
DP: 80
P5
P6
P3
D-IP:C
S-IP: A
D-IP:C
S-IP: B
SP: 5775
DP: 80
D-IP:C
S-IP: B

## Slide 53: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 54: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 55: Principles of Reliable data transfer
important in app., transport, link layers
top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 56: Reliable data transfer: getting started
send
side
receive
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 57: Reliable data transfer: getting started
We’ll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow on both directions!
use finite state machines (FSM) to specify sender, receiver
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions

## Slide 58: Rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver read data from underlying channel
Wait for call from above
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
extract (packet,data)
deliver_data(data)
Wait for call from below
rdt_rcv(packet)
sender
receiver

## Slide 59: Rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  receiver feedback: control msgs (ACK,NAK) rcvr->sender

## Slide 60: rdt2.0: FSM specification
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
sender
receiver
rdt_send(data)
L

## Slide 61: rdt2.0: operation with no errors
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 62: rdt2.0: error scenario
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 63: rdt2.0 has a fatal flaw!
What happens if ACK/NAK corrupted?
sender doesn’t know what happened at receiver!
can’t just retransmit: possible duplicate
Handling duplicates:
sender retransmits current pkt if ACK/NAK garbled
sender adds sequence number to each pkt
receiver discards (doesn’t deliver up) duplicate pkt
Sender sends one packet,
then waits for receiver
response
stop and wait

## Slide 64: rdt2.1: sender, handles garbled ACK/NAKs
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK 0
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
Wait for
call 1 from above
Wait for ACK or NAK 1
L
L

## Slide 65: rdt2.1: receiver, handles garbled ACK/NAKs
Wait for
0 from below
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)

## Slide 66: rdt2.1: discussion
Sender:
seq # added to pkt
two seq. #’s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “current” pkt has 0 or 1 seq. #
Receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender

## Slide 67: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 68: rdt2.2: sender, receiver fragments
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
Wait for ACK
0
sender FSM
fragment
Wait for
0 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
has_seq1(rcvpkt))
sndpkt = make_pkt(ACK,chksum)
udt_send(sndpkt)
receiver FSM
fragment
L

## Slide 69: rdt3.0: channels with errors and loss
New assumption: underlying channel can also lose packets (data or ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help, but not enough
Approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
  retransmission will be duplicate, but use of seq. #’s already handles this
  receiver must specify seq # of pkt being ACKed
requires countdown timer

## Slide 70: rdt3.0 sender
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for ACK0
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
stop_timer
udt_send(sndpkt)
start_timer
timeout
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt)
Wait for
call 0from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
L
L
L

## Slide 71: rdt3.0 in action

## Slide 72: rdt3.0 in action

## Slide 73: Performance of rdt3.0
rdt3.0 works, but performance stinks
example: 1 Gbps link, 15 ms e-e prop. delay, 1KB packet:
T
transmit
=
8kb/pkt
10**9 b/sec
= 8 microsec
  U sender: utilization – fraction of time sender busy sending
L (packet length in bits)
R (transmission rate, bps)
=
  1KB pkt every 30 msec -> 33kB/sec thruput over 1 Gbps link
  network protocol limits use of physical resources!

## Slide 74: rdt3.0: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R

## Slide 75: Pipelined protocols
Pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver
Two generic forms of pipelined protocols: go-Back-N, selective repeat

## Slide 76: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
Increase utilization
by a factor of 3!

## Slide 77: Go-Back-N
Sender:
k-bit seq # in pkt header
“window” of up to N, consecutive unack’ed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK”
  may receive duplicate ACKs (see receiver)
timer for each in-flight pkt
timeout(n): retransmit pkt n and all higher seq # pkts in window

## Slide 78: GBN: sender extended FSM
Wait
start_timer
udt_send(sndpkt[base])
udt_send(sndpkt[base+1])
…
udt_send(sndpkt[nextseqnum-1])
timeout
rdt_send(data)
if (nextseqnum < base+N) {
sndpkt[nextseqnum] = make_pkt(nextseqnum,data,chksum)
udt_send(sndpkt[nextseqnum])
if (base == nextseqnum)
start_timer
nextseqnum++
}
else
refuse_data(data)
base = getacknum(rcvpkt)+1
If (base == nextseqnum)
stop_timer
else
start_timer
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
base=1
nextseqnum=1
rdt_rcv(rcvpkt)
&& corrupt(rcvpkt)
L

## Slide 79: GBN: receiver extended FSM
ACK-only: always send ACK for correctly-received pkt with highest in-order seq #
  may generate duplicate ACKs
  need only remember expectedseqnum
out-of-order pkt:
  discard (don’t buffer) -> no receiver buffering!
  Re-ACK pkt with highest in-order seq #
Wait
udt_send(sndpkt)
default
rdt_rcv(rcvpkt)
&& notcurrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum)
udt_send(sndpkt)
expectedseqnum++
expectedseqnum=1
sndpkt =
make_pkt(expectedseqnum,ACK,chksum)
L

## Slide 80: GBN in action

## Slide 81: Selective Repeat
receiver individually acknowledges all correctly received pkts
  buffers pkts, as needed, for eventual in-order delivery to upper layer
sender only resends pkts for which ACK not received
  sender timer for each unACKed pkt
sender window
  N consecutive seq #’s
  again limits seq #s of sent, unACKed pkts

## Slide 82: Selective repeat: sender, receiver windows

## Slide 83: Selective repeat
data from above :
if next available seq # in window, send pkt
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N]:
mark pkt n as received
if n is the smallest unACKed pkt, advance window base to next unACKed seq #
sender
pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
receiver

## Slide 84: Selective repeat in action

## Slide 85: Selective repeat: dilemma
Example:
seq #’s: 0, 1, 2, 3
window size=3
receiver sees no difference in two scenarios!
incorrectly passes duplicate data as new in (a)

## Slide 86: UDP checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later ….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment

## Slide 87: Internet Checksum Example
Note
  When adding numbers, a carryout from the most significant bit needs to be added to the result
Example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit

## Slide 88: TCP: Overview RFCs: 793, 1122, 1323, 2018, 2581
full duplex data:
  bi-directional data flow in same connection
  MSS: maximum segment size
connection-oriented:
  handshaking (exchange of control msgs) init’s sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte steam:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
send & receive buffers

## Slide 89: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pnter
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 90: TCP Round Trip Time and Timeout
Q: how to set TCP timeout value?
longer than RTT
  but RTT varies
too short: premature timeout
  unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  average several recent measurements, not just current SampleRTT

## Slide 91: TCP Round Trip Time and Timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
Exponential weighted moving average
influence of past sample decreases exponentially fast
typical value:  = 0.125

## Slide 92: Example RTT estimation:

## Slide 93: TCP Round Trip Time and Timeout
Setting the timeout
EstimtedRTT plus “safety margin”
  large variation in EstimatedRTT -> larger safety margin
first estimate of how much SampleRTT deviates from EstimatedRTT:
TimeoutInterval = EstimatedRTT + 4*DevRTT
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
Then set timeout interval:

## Slide 94: TCP reliable data transfer
TCP creates rdt service on top of IP’s unreliable service
Pipelined segments
Cumulative acks
TCP uses single retransmission timer
Retransmissions are triggered by:
  timeout events
  duplicate acks
Initially consider simplified TCP sender:
  ignore duplicate acks
  ignore flow control, congestion control

## Slide 95: TCP sender events:
data rcvd from app:
Create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running (think of timer as for oldest unacked segment)
expiration interval: TimeOutInterval
timeout:
retransmit segment that caused timeout
restart timer (double)
Ack rcvd:
If acknowledges previously unacked segments
  update what is known to be acked
  start timer if there are outstanding segments

## Slide 96: TCP: retransmission scenarios
Host A
Seq=100, 20 bytes data
ACK=100
time
premature timeout
Host B
Seq=92, 8 bytes data
ACK=120
Seq=92, 8 bytes data
Seq=92 timeout
ACK=120
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
lost ACK scenario
Host B
X
Seq=92, 8 bytes data
ACK=100
time
Seq=92 timeout
SendBase
= 100
SendBase
= 120
SendBase
= 120
Sendbase
= 100

## Slide 97: TCP retransmission scenarios (more)
Host A
Seq=92, 8 bytes data
ACK=100
loss
timeout
Cumulative ACK scenario
Host B
X
Seq=100, 20 bytes data
ACK=120
time
SendBase
= 120

## Slide 98: TCP ACK generation [RFC 1122, RFC 2581]
Event at Receiver
Arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
Arrival of in-order segment with
expected seq #. One other
segment has ACK pending
Arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
Arrival of segment that
partially or completely fills gap
TCP Receiver action
Delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
Immediately send single cumulative
ACK, ACKing both in-order segments
Immediately send duplicate ACK,
indicating seq. # of next expected byte
Immediately send ACK, provided that
segment startsat lower end of gap

## Slide 99: Fast Retransmit
Time-out period often relatively long:
  long delay before resending lost packet
Detect lost segments via duplicate ACKs.
  Sender often sends many segments back-to-back
  If segment is lost, there will likely be many duplicate ACKs.
If sender receives 3 ACKs for the same data, it supposes that segment after ACKed data was lost:
  fast retransmit: resend segment before timer expires

## Slide 100: TCP Flow Control
receiver side of TCP connection has a receive buffer:
speed-matching service: matching the send rate to the receiving app’s drain rate
app process may be slow at reading from buffer
sender won’t overflow
receiver’s buffer by
transmitting too much,
too fast
flow control

## Slide 101: TCP Flow control: how it works
(Suppose TCP receiver discards out-of-order segments)
spare room in buffer
= RcvWindow
= RcvBuffer-[LastByteRcvd - LastByteRead]
Rcvr advertises spare room by including value of RcvWindow in segments
Sender limits unACKed data to RcvWindow
  guarantees receive buffer doesn’t overflow

## Slide 102: TCP Connection Management
Recall: TCP sender, receiver establish “connection” before exchanging data segments
initialize TCP variables:
  seq. #s
  buffers, flow control info (e.g. RcvWindow)
client: connection initiator
Socket clientSocket = new Socket("hostname","port number");
server: contacted by client
Socket connectionSocket = welcomeSocket.accept();
Three way handshake:
Step 1: client host sends TCP SYN segment to server
  specifies initial seq #
  no data
Step 2: server host receives SYN, replies with SYNACK segment
  server allocates buffers
  specifies server initial seq. #
Step 3: client receives SYNACK, replies with ACK segment, which may contain data

## Slide 103: TCP Connection Management (cont.)
Closing a connection:
client closes socket: clientSocket.close();
Step 1: client end system sends TCP FIN control segment to server
Step 2: server receives FIN, replies with ACK. Closes connection, sends FIN.
client
FIN
server
ACK
ACK
FIN
close
close
closed
timed wait

## Slide 104: TCP Connection Management (cont.)
Step 3: client receives FIN, replies with ACK.
  Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
client
FIN
server
ACK
ACK
FIN
closing
closing
closed
timed wait
closed

## Slide 105: TCP Connection Management (cont)
TCP client
lifecycle
TCP server
lifecycle

## Slide 106: Principles of Congestion Control
Congestion:
informally: “too many sources sending too much data too fast for network to handle”
different from flow control!
manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)
a top-10 problem!

## Slide 107: Approaches towards congestion control
End-end congestion control:
no explicit feedback from network
congestion inferred from end-system observed loss, delay
approach taken by TCP
Network-assisted congestion control:
routers provide feedback to end systems
  single bit indicating congestion (SNA, DECbit, TCP/IP ECN, ATM)
  explicit rate sender should send at
Two broad approaches towards congestion control:

## Slide 108: Congestion control concepts
Congetion window (CongWin):
Different from RcvWindow
Determined by the actual congestion control algorithm
Usually smaller than RcvWindow.
At the sender:
LastByteSent – LastByteAcked <= min(CongWin, RcvWindow)
<= CongWin
Throughput:
CongWin/RTT Bytes/sec
Adjusting CongWin changes the transmission rate and therefore throughput
TCP is self-clocking – uses ACKs to trigger (clock) its increase in congestion window size

## Slide 109: Congestion control Components
Additive-increase, multiplicative-decrese: (AIMD)
Control the change of CongWin
Increase when the ACK is received as expected
  Indication of no congestion
  Explore the highest possible bandwidth
Decrease when loss occurs
  Indication of congestion
  Reduce transmission rate to a sufficiently low value to avoid congestion
Slow start:
How to avoid congestion control
Reaction to timeout events:
How to deal with network congestion

## Slide 110: Additive increase, multiplicative decrease
Approach: increase transmission rate (window size), probing for usable bandwidth, until loss occurs
  additive increase: increase CongWin by 1 MSS (Maximum Segment Size) every RTT until loss detected
  multiplicative decrease: cut CongWin in half after loss
time
congestion window size
Saw tooth
behavior: probing
for bandwidth

## Slide 111: TCP Congestion Control: details
How does sender perceive congestion?
loss event = timeout or 3 duplicate acks
TCP sender reduces rate (CongWin) after loss event
Problem:
This linear increase of CongWin is a waste of bandwidth if the network resource is huge!
Why not increase it exponentially and see what happens?
Solution?
Slow Start (starting from a slow rate)
Increase 1 MSS for each ACKed segment, therefore double the congWin every time.

## Slide 112: TCP Slow Start
When connection begins, CongWin = 1 MSS
  Example: MSS = 500 bytes & RTT = 200 msec
  initial rate = 20 kbps
increase rate exponentially until first loss event:
  double CongWin every RTT
  done by incrementing CongWin for every ACK received
Summary: initial rate is slow but ramps up exponentially fast
Problem?
  May create problem when transmission rate approaches to the network capacity
  Switch to linear instead
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 113: TCP Slow Start - Refinement
Q: When should the exponential increase switch to linear?
A: When CongWin gets to 1/2 of its value before timeout.
Implementation:
Variable Threshold
At loss event, Threshold is set to 1/2 of CongWin just before loss event
Loss events:
3 duplicative ACKs
  Packet(s) have been lost
  However, network is able to deliver 3 ACKs, so it is still capable of transmitting packets, i.e., no serious congestion!
Timeout
  NO ACK can be sent back, i.e., network congested!
Conclusion: These two events should be treated differently!

## Slide 114: Two versions
TCP Tahoe: (early version)
Slow start begins after either of
  3 Successive ACKs
  Timeout
TCP Reno: (improved version)
Slow start begins only after
  Timeout
Cancels the slow-start phase after a triple duplicate ACKs – known as Fast Recovery.

## Slide 115: Two versions

## Slide 116: Summary of TCP Reno
After 3 dup ACKs:
  CongWin is cut in half
  window then grows linearly
But after timeout event:
  CongWin instead set to 1 MSS;
  window then grows exponentially
  to a threshold, then grows linearly
Two phases:
  When CongWin is below Threshold, sender in slow-start phase, window grows exponentially.
  When CongWin is above Threshold, sender is in congestion-avoidance phase, window grows linearly.

## Slide 117: TCP sender congestion control
State | Event | TCP Sender Action | Commentary
Slow Start (SS) | ACK receipt for previously unacked data | CongWin = 2*CongWin, If (CongWin > Threshold) set state to “Congestion Avoidance” | Resulting in a doubling of CongWin every RTT
Congestion Avoidance (CA) | ACK receipt for previously unacked data | CongWin = CongWin+MSS * (MSS/CongWin) | Additive increase, resulting in increase of CongWin by 1 MSS every RTT
SS or CA | Loss event detected by triple duplicate ACK | Threshold = CongWin/2, CongWin = Threshold, Set state to “Congestion Avoidance” | Fast recovery, implementing multiplicative decrease. CongWin will not drop below 1 MSS.
SS or CA | Timeout | Threshold = CongWin/2, CongWin = 1 MSS, Set state to “Slow Start” | Enter slow start
SS or CA | Duplicate ACK | Increment duplicate ACK count for segment being acked | CongWin and Threshold not changed

## Slide 118: TCP throughput
What’s the average throughout of TCP as a function of window size and RTT?
  Ignore slow start
Let W be the window size when loss occurs.
When window is W, throughput is W/RTT
Just after loss, window drops to W/2, throughput to W/2RTT.
Average throughout: .75 W/RTT

## Slide 119: TCP Futures: TCP over “long, fat pipes”
Example: 1500 byte segments, 100ms RTT, want 10 Gbps throughput
Requires window size W = 83,333 in-flight segments
Throughput in terms of loss rate:
➜ L = 2·10-10 Wow
New versions of TCP for high-speed needed!

## Slide 120: TCP vs Multimedia Applications
Multimedia apps often do not use TCP
  do not want rate throttled by congestion control
Instead use UDP:
  pump audio/video at constant rate, tolerate packet loss
Research area: TCP friendly
  Provide bandwidth to TCP if multimedia streaming is not there
Nothing prevents app from opening parallel connections between 2 hosts.
  May generate huge traffic
Web browsers do this
  May easily eat out network bandwidth and affect multimedia Streaming
Research topic: Service differentiation
  Provision network resource such that TCP traffic does not affect multimedia streaming significantly.